## Slide 1: System Processors & CPU Architecture Summary System Processors CPU Architecture - RISC and CISC Architecture Introduction to Graphics Processors

## Slide 2: System Processors
Both families use x86 instruction set
  CPU hardware very different between Intel & AMD
  software compatible
Intel – Core i3 (low end), i5 (mid range), i7 (high end) ,
  - i9 (higher performance for gamers/PC enthusiasts)
AMD
  first to bring 64 bit CPU to desktop
  first to attach memory directly to CPU
  first to offer desktop multicore CPUs

## Slide 3: Sample x86 Assembler
.model small
.stack 100h
.data msg db 'Hello world!$’
.code
start: mov ah, 09h ; Display the message lea dx, msg int 21h mov ax, 4C00h ; Terminate the executable int 21h
end start
From Wikipedia
https://www.cs.virginia.edu/~evans/cs216/guides/x86.html

## Slide 4: System Processors
Advanced RISC Machines (ARM)-Mobile Architecture https://versus.com/en/arm-cortex-a53-vs-arm-cortex-a57 designer of a popular low-power CPU (not a manufacturer)
  used in smart phones, tablets, embedded systems
  not x86 compatible
  some chip designs have heterogeneous cores
    low-power, low-performance cores (A53) teamed with more powerful but more power-hungry cores (A57).
    cores activated or deactivated according to processor workload
    very efficient use of electricity

## Slide 5: Processor Sockets
CPUs sit in a motherboard socket
  motherboard socket has pins, CPU connects with the pins
  since Core and Athlon CPUs have different designs, they have different socket designs
  newer CPUs might not be supported by older motherboards

## Slide 6: CPU Architecture
What does a CPU do?
Grab and execute program instructions
All done over a datapath A datapath has many functional units
We will look at some key ones in the next slide. Another important term to understand is IPC.
Instructions per clock tick (IPC)
  amount of work performed per clock tick
  some designs have fast clock ticks but lower IPC
  faster clock speeds consume more energy

## Slide 7: CPU
Arithmetic Logic Unit (ALU) performs arithmetic and logic functions
Registers - high speed ‘scratch pad’ to store data currently being processed
Memory Buffer (Data) Register (MBR,MDR) – stores data just received from, or about to be written to memory
Memory Access Register (MAR) – stores address of memory to be accessed next
Program Counter (PC) – stores address of next instruction

## Slide 8: Fetch Execute Cycle
Fetch
  Copy PC to MAR
  Get instruction into MDR
Decode
  Identify operation and operands
Execute
  Carry out instruction
  May require additional memory fetches
Store
  Put data to be stored in MDR
  Put location into MAR

## Slide 9: Instruction Pipelining
Instruction pipelining (superscalar architectures)
- analogous to an assembly line, where each worker on the line does a small amount of work building an item (say, a car), which moves down the line from one worker to another
- basic instruction cycle (fetch, decode, execute, store) can be pipelined (e.g. while one instruction is being executed, another is being decoded) - steps in the instruction cycle can be broken down into micro-ops that can be pipelined - length of pipeline is called its depth

## Slide 10: Instruction Pipelining Pipelining enhances throughput – - individual instruction do not run any faster - for example

## Slide 11: Real World Example We assume that each such bicycle part is available in stock. Assume that each of the 7 stages of production takes 6 minutes

## Slide 12: Real World Example cont’d Then it is simple arithmetic to conclude that — from the ﬁrst stage to the last — it takes a total of 42 minutes to fully assemble a bicycle. But it should also be equally simple to conclude that the factory produces one bicycle every 6 minutes. Once the pipeline is full – a bicycle every 6 minutes!
 | Bicycle 1 | Bicycle 2 | Bicycle 3 | Bicycle 4 | Bicycle 5 | Bicycle 6 | Bicycle 7 | Bicycle 8 | Bicycle 9
WS1 | B1 | B2 | B3 | B4 | B5 | B6 | B7 | B8 | B9
WS2 |  | B1 | B2 | B3 | B4 | B5 | B6 | B7 | B8
WS3 |  |  | B1 | B2 | B3 | B4 | B5 | B6 | B7
WS4 |  |  |  | B1 | B2 | B3 | B4 | B5 | B6
WS5 |  |  |  |  | B1 | B2 | B3 | B4 | B5
WS6 |  |  |  |  |  | B1 | B2 | B3 | B4
WS7 |  |  |  |  |  |  | B1 | B2 | B3

## Slide 13: Real World Example cont’d Suppose that — for some reason — the fifth stage remains idle for one time slot of 6 minutes. This is a “stall” in the pipeline. Clearly then, in the subsequent consecutive time slots, this idle time of 6 minutes — which we may call a ‘bubble’ — will pass through each of the remaining 3 stages of the pipeline.
 | Bicycle 1 | Bicycle 2 | Bicycle 3 | Bicycle 4 | Bicycle 5 | Bicycle 6 | Bicycle 7 | Bicycle 8 | Bicycle 9
WS1 | B1 | B2 | B3 | B4 | B5 | B6 | B7 | B8 | B9
WS2 |  | B1 | B2 | B3 | B4 | B5 | B6 | B7 | B8
WS3 |  |  | B1 | B2 | B3 | B4 | B5 | B6 | B7
WS4 |  |  |  | B1 | B2 | B3 | B4 | B5 | B6
WS5 |  |  |  |  | Bubble | B1 | B2 | B3 | B4
WS6 |  |  |  |  |  | Bubble | B1 | B2 | B3
WS7 |  |  |  |  |  |  | Bubble | B1 | B2

## Slide 14: CPU Architecture
Pipelines may stall
  e.g. an instruction need to wait for memory
  causes a ‘bubble’ in the pipeline where no work is being done
Branch Prediction
  CPU estimates what future instructions will be, and performs them inside a pipeline stall or other ‘spare time’
  quite good predictions possible, but not perfect
Out of Order Execution
  instructions re-arranged in pipeline to reduce overall processing time and minimise stalls

## Slide 15: CPU Architecture
Symmetric Multiprocessing
  CPU has more than one (identical) core
    e.g. Intel Core i7 series has 2, 4, (4 is most common) or 6 cores , note i9 series can have 10 cores
  cores work in parallel
  thus more than one instruction executed at once

## Slide 16: CPU Architecture
https://www.crn.com/news/components-peripherals/new-intel-core-desktop-cpus-pack-up-to-5-3ghz-10-cores
https://ark.intel.com/content/www/us/en/ark/products/199332/intel-core-i9-10900k-processor-20m-cache-up-to-5-30-ghz.html

## Slide 17: RISC and CISC Architecture
CPU architecture can be broadly classified into two different types:
  CISC – Complex Instruction Set Computer
  RISC – Reduced Instruction Set Computer
Another distinction that can be made is the Von Neumann model memory vs the Harvard memory model
http://www.differencebetween.net/technology/difference-between-von-neumann-and-harvard-architecture/#:~:text=Unlike%20Von%20Neumann%20architecture%20which,the%20way%20they%20access%20memories.

## Slide 18: Von Neumann Model versus Harvard Model
Von Neumann Model
Harvard Model
Separate buses for data and
instructions

## Slide 19: CISC – Complex Instruction Set Computer
When modern CPU’s were first developed, memory was very expensive
Programs could be smaller if instructions were more powerful and could perform multiple operations
Example:
  Multiply two numbers together store the result.
  HLL: c = a * b;
  CISC MULT A,B,C

## Slide 20: CISC
Multiple operations lead to many different kinds of instructions that access memory
This results in variable length instructions and fetch-decode-execute time unpredictability
– making it more complex
Thus hardware handles the complexity
x86 hardware is like this

## Slide 21: RISC
Attempt to make architecture simpler
Reduced number of instructions in the instruction set
Need more instructions to do the same thing compared to CISC
Try to reduce the number of memory accesses required by increasing the number of registers
The multiply example would become:
LOAD A,1 LOAD B,2 MULT 1,2 STORE 1,C

## Slide 22: RISC
A RISC processor will generally have:
A large number of general purpose registers
A small number of instructions with the same format
Optimisation of instruction pipeline
Uniform instruction size and format should make pipelining easier

## Slide 23: RISC
 | CISC processor Intel 80486 | RISC processor Sun SPARC
Year developed | 1989 | 1987
No. instructions | 235 | 69
Instruction Size (bytes) | 1-11 | 4
Addressing modes | 11 | 1
GP Registers | 8 | 40-520

## Slide 24: Which is faster?
Program Time = (Cycle Time X Cycles per Instruction) X no of instructions in program
=> Program Time = (Cycle Time / IPC ) X no of instructions in program

## Slide 25: CISC versus RISC
CISC | RISC
Emphasis on hardware | Emphasis on software
Multiple instruction sizes and formats | Instructions of same set with few formats
Less Registers | Uses more registers
More addressing modes | Fewer addressing modes
Extensive use of microprogramming | Complexity in compiler
Instructions take varying amount of cycle time | Instructions take one cycle time
Pipelining was difficult in the past but CISC has been redesigned and pipelining has been added. | Pipelining is easy
RISC
  each instruction takes the same time,
  simpler architecture-> smaller, faster, more cache

## Slide 26: CPU Architecture - Multicores
Computation speed-up of a task not linear
  many problems are not 100% parallelisable
  overhead involved in coordinating sharing of work between cores
  access to memory must be coordinated
  keeping each core’s cache consistent is difficult
Often each core is performing a different task

## Slide 27: CPU Architecture –Introduction to Threads
A thread is a basic unit of CPU utilisation.
A thread would execute a particular sequence of instructions of the process e.g., handling the “graphics” instructions of a mobile phone.
You can have a traditional (heavyweight) single-threaded process (since it is similar to a real process but executes within the context of a process and shares the same resources allotted to the process by the kernel) or a multi-threaded process.

## Slide 28: CPU Architecture -SMT
Simultaneous Multithreading (SMT)
  pipeline stalls are inevitable – so use that wasted CPU time
  use stalls in running one thread of execution to run another thread of execution
  operating system thus sees a single core as two logical cores, and schedules different tasks to each
  example: Intel’s Hyper-threading

## Slide 29: CPU Architecture-Hyper-Threading

## Slide 30: CPU Architecture-Hyper-Threading
Note they are equivalent- same number of green and blue processing execution units for the 2 threads.
"Throughput" for the SMT will be greater assuming there are no "bottlenecks". In SMT the 2 threads are doing work in the bubbles- the white squares.
A "system programmer" - in charge of writing software for "operating systems" has written an algorithm to handle 2 threads like this. The SMT diagram seems a reasonable result for such an algorithm.

## Slide 31: Other Processing Models
In the “standard” CPU model, the CPU executes one instruction at a time, operating on one piece of data
Eg
Load A ,1 Load B, 2
This is known as a Single Instruction, Single Data or SISD computer

## Slide 32: Parallel Processing
Some applications, especially graphics related, perform the same calculations many times, but on different data
This type of processing can be made much faster if we are able to perform the same calculation on many different pieces of data at once
To see how this can work we first need a basic understanding of the main steps involved in graphics processing…

## Slide 33: Graphics Processing
Ultimate goal: display a series of images on a screen (2D)
Images consist of pixels, which have colour and brightness
However the internal model of an image is a collection of 3D objects and a lighting source

## Slide 34: Graphics Processing
Shapes are represented as coordinates in 3D space)

## Slide 35: Graphics
We also have some shading, or texture information to add in

## Slide 36: Graphics
Surfaces are normally broken up into triangles, and these are very easy to manipulate mathematically.
Curved surfaces are approximated by using a very large number of triangles

## Slide 37: Graphics
As the “camera” or view changes the objects need to be rotated around an arbitrary point
The change in position can be calculated by applying a rotation matrix to all of the vertices (i.e. same instructions applied to a large amount of data)

## Slide 38: Perspective
Once rotation is complete, we need to determine which objects, or parts of objects are visible from a given position (Camera Position)
This requires calculating points of intersection
Again same calculations applied to lots of different data

## Slide 39: Perspective
All these steps involve lots of calculations on three dimensional coordinates, and hence a lot of matrix calculations
However in many cases the same calculation is repeated performed on different data

## Slide 40: SIMD
In a Single Instruction Multiple Data Computer model, one instruction can operate on multiple data sets

## Slide 41: SIMD
This is implemented as multiple processors that each follow the same instructions, but have some local memory where they can store the data it is working on

## Slide 42: CPU vs GPU
A typical GPU has many more processors compared to a CPU

## Slide 43: Nvida Maxwell Architechure

## Slide 44: SIMD
SIMD processors are particularly useful in applications where the same operation needs to be applied to large amounts of data such as
Digital Signal Processing (DSP)
Computer Graphics
https://docs.nvidia.com/cuda/maxwell-tuning-guide/index.html
https://techterms.com/definition/cuda#:~:text=CUDA,both%20the%20CPU%20and%20GPU.&text=While%20CUDA%20only%20supports%20NVIDIA,with%20several%20different%20programming%20languages
http://download.nvidia.com/developer/cuda/seminar/TDCI_Arch.pdf https://www.techwalla.com/articles/128-bit-vs-256-bit-graphics-card