## Slide 1: Digital Logic & Boolean Algebra Interesting bit flipping video youtube.com/watch?v=AaZ_RSt0KP8 Summary • NOT, AND, OR, XOR Boolean operations and logic gates • Basic Logic Circuits and Truth Tables • Bit Masking Operations

## Slide 2: Digital Logic & Boolean Algebra
Binary can be considered as truth values:
  0 = False, 1 = True
Boolean Algebra: the laws of algebra for truth values
  consists of operations on truth values, the result of which is another truth value
  fundamental for the design of logic circuits and for tests in computer programming
  CPU hardware consists of circuits built from logic gates – logic gates perform Boolean Algebra
George Boole(/buːl/; 2 November 1815–8 December 1864) was a largely self-taught English mathematician, philosopher and logician, most of whose short career was spent as the first professor of mathematics at Queen's College, Cork in Ireland. He worked in the fields of differential equations and algebraic logic and is best known as the author of The Laws of Thought(1854) which contains Boolean algebra. -from Wikipedia

## Slide 3: Gates and Transistors
Logic gates are made up of transistors
Remember that a transistor is just a switch that can be open or closed.
https://www.electronics-tutorials.ws/transistor/tran_4.html
If open, no current flows (“0”)
If closed, current flows (“1”)
Two basic types
  Current used to turn the switch on (off be default) NPN transistor
  Current used to turn the switch off (on by default) PNP transistor

## Slide 4: Gates and Transistors cont’d

## Slide 5: Boolean Algebra
Boolean Operator: NOT
  NOT returns the opposite value
i.e., True becomes False, False becomes True
NOT(written as /A or -A or sometimes !A or A or ~A
A | /A
1 | 0
0 | 1

## Slide 7: AND Gate
AND is true when both inputs are true
  written as x.y or sometimes x ∧ y or as xy
A | B | X =A.B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 8: Basic AND Gate Design Using Transistors

## Slide 9: OR Gate
OR is true when any input is true – written (confusingly!) as x+y or sometimes x∨y – Sometimes referred to as inclusive or
A | B | X =A+B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 10: Basic OR Gate Design Using Transistors

## Slide 11: XOR Gate
XOR (exclusive OR) is similar to OR, except it is true when only one, and exclusively one, input is true – written as
X = A ⊕ B.
A | B | X = A ⊕ B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 12: Logic Gates
Computer hardware is made from logic gates
  Basic logic gates: AND, OR, NOT
  Derived negated gates: NAND, NOR, XOR, XNOR
Any logic circuits can be build from combinations of just AND, OR, NOT – alternatively, use just NAND, NOR

## Slide 13: Logic Gates
NOR gate
NAND gate
Q=/(A+B)
out= /(A.B)

## Slide 14: Logic Circuits
A.B+C (usual order of precedence)
A.B+C.D

## Slide 15: Creating a Truth Table

## Slide 16: Creating the Truth Table
A | B | C | B.C | /A | /A+B.C | /(/A+B.C) | A.B | /(/A+.B.C).A.B | /C | A.B./C
0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0
0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0
The 2 circuits are logically equivalent because the final columns are identical.

## Slide 17: Simplifying a Circuit using the Boolean Algebra Rules, (Laws)

## Slide 18: Boolean Algebra Rules, (Laws) https://www.electronics-tutorials.ws/boolean/bool_6.html
Boolean Algebra Rules
Commutative Laws | A+B =B+A and A.B=B.A
Associative Laws | A+(B+C)= A+B+C=(A+B)+C A.(B.C) = (A.B).C
Distributive Laws | A.(B+C) =A.B+A.C A+B.C = (A+B).(A+C)
De Morgan’s Laws | /(A+B) =/A./B and /(A.B) =/A+/B
Idempotent Laws | A+A=A and A.A=A
Absorption Laws | A+A.B= A and A.(A+B)= A
Involation Law –Double Negation | //A = A
Identity Laws | A+0 = A and A.1 =A
Annulment Laws | A+1 = 1 and A.0 = 0
Complementary Laws | A+/A = 1 and A./A= 0
Special Identity Law | A.B + /A.B = B

## Slide 19: Simplifying a Circuit using the Boolean Algebra Rules, (Laws)
/(/A + (B.C)) . A.B (Output of circuit a)
De Morgan's Law: //A ./(B.C). A.B
The //A= A Law : => A ./(B.C). A.B
The Commutative Law, X.Y=Y.X => A .A. /(B.C). B
The Idempotent Law , A.A = A : = >A. /(B.C). B
The Commutative Law X.Y=Y.X=>A.B./(B.C)
De Morgan’s Law => A.B.(/B+/C)
The Distributive Law =>A.B.(/B+/C) = A.B./B + A.B./C
The Complement Law, B./B =0 and Annulment Law D.0=0 and Identity Law D+0=D: => A.B./C
This is circuit b) !
Therefore, the 2 circuits are logically equivalent.

## Slide 20: Moore’s Law
In 1965, Gordon Moore, founder of Fairchild, and then Intel predicted that the number of transistors per unit or area would double every two years.

## Slide 21: The Evolution of CPU’s

## Slide 22: More Minaturisation changes during last decade…
… and Price

## Slide 23: Logic Circuits-Half Adder
Say we wanted to construct an adder, which adds two bits together and outputs the sum (as a single bit) and a carry bit – called a half adder
– truth table:
A | B | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Sum is A ⊕ B.
Carry is A.B

## Slide 24: Logic circuits – Full Adder
We could combine two half adders to make a full adder (which accepts 3 inputs: A, B and a carry-in)
Full adders can be cascaded together to make a parallel adder that can add multi-bit binary numbers

## Slide 25: Logic circuits – Full Adder
We can build a truth table to examine the behaviour of the full-adder

## Slide 26: Logic circuits –Truth Table for the Full Adder
A | B | C (cin ) | V=A XOR B | W=Sum =V XOR C | X=V AND C | Y=A AND B | Z=Cout=X OR Y
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1` | 0 | 1 | 0 | 1
1 | 0 | 0 | 1 | 1 | 0 | 0 | 0
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 0 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | 1 | 1

## Slide 27: Logic Circuits –Parallel Adder
Parallel adder example
4 cascaded full-adders to add two 4-bit binary numbers
the carry-out of each full-adder feeds into carry-in of the next full-adder
the first carry-in is set to 0

## Slide 28: Bit Masking
Bit masks uses Boolean operations to access individual bits from binary data
Used in ‘low level’ programming
  device drivers and other hardware configuration/communication
  data packet encoding/decoding
  low level graphics
  Switching LEDs on and off (Arduino)

## Slide 29: Bit Masking- Resetting a Particular Bit
To reset (i.e. make 0) a bit in a byte, A, AND it with a mask of all 1’s except the bit to reset e.g. reset the LSB (bit 0) of any byte A:
A = XXXX XXXX2, where X is 0 or 1
A AND M= XXXX XXXX2 AND 1111 11102= XXXX XXX02
–
Bit No | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
A | X | X | X | X | X | X | X | X
BITWISE AND | & | & | & | & | & | & | & | &
Mask =M | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
A AND M | X | X | X | X | X | X | X | 0

## Slide 30: Bit Masking- e.g. Resetting a Particular Bit, bit 0
Example byte: 1000 11012 = 8D16
In Java:
short data = 0x8D;
short bitmask = 0xFE;
short result = (short) (data & bitmask); System.out.println(String.format("%x",result));
Bit No | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
E(EXAMPLE) | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1
BITWISE AND | & | & | & | & | & | & | & | &
Mask =M | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
E AND M | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 0

## Slide 31: Bit Masking- Setting a Particular Bit
To set (i.e. make 1) a bit in a byte, OR it with a mask of all 0’s except the bit to set e.g. set bit 4 :
A = XXXX XXXX2, where X is 0 or 1
A OR M= XXXX XXXX2 OR 0001 00002= XXX1 XXXX2
Bit No | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
A | X | X | X | X | X | X | X | X
BITWISE OR | ¦ | ¦ | ¦ | ¦ | ¦ | ¦ | ¦ | ¦
Mask =M | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
A OR M | X | X | X | 1 | X | X | X | X

## Slide 32: Bit Masking- e.g. Setting a Particular Bit, bit 4
Example byte: 1000 11012 = 8D16
In Java:
short data = 0x8D;
short bitmask = 0x10;
short result = (short) (data | bitmask); System.out.println(String.format("%x",result));
Bit No | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
E(EXAMPLE) | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1
BITWISE OR | ¦ | ¦ | ¦ | ¦ | ¦ | ¦ | ¦ | ¦
Mask =M | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
E OR M | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1

## Slide 33: Bit Masking- “Flipping”/Toggling a bit
To flip a bit in a byte (0->1, 1->0), XOR it with a mask of all 0’s except the bits to flip e.g., flip the bits 2 and 3 of A, any byte.
A = XXXX XXXX2, where X is 0 or 1
A XOR M= XXXX XXXX2 OR 0000 11002= XXXX /X/XXX2
–
Bit No | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
A | X | X | X | X | X | X | X | X
BITWISE XOR | ^ | ^ | ^ | ^ | ^ | ^ | ^ | ^
Mask =M | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0
A XOR M | X | X | X | X | /X | /X | X | X

## Slide 34: Bit Masking- e.g. Flipping Particular Bits, bits 2 and 3
Example byte: 1000 01012 = 8516
In Java:
short data = 0x85;
short bitmask = 0x0C;
short result = (short) (data | bitmask); System.out.println(String.format("%x",result));
Bit No | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
E(EXAMPLE) | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1
BITWISE XOR | ^ | ^ | ^ | ^ | ^ | ^ | ^ | ^
Mask =M | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0
E XOR M | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1